## Slide 1: Epileptic Seizure Detection in Continuous EEG
BM 4151 Biosignal Processing

## Slide 2: Objective
Detect epileptic seizure events in continuous EEG
  Use signal analysis techniques to extract features
  Develop a classification algorithm with high accuracy
Use dimensionality reduction for robust computation
Use manual and automatic feature extraction
Minimize the number of false detections
  Defined as detecting 2 consecutive windows being detected as seizures

## Slide 3: Dataset
CHB-MIT Scalp EEG Database in physionet.org [1]
EEG data for 23 patients, average of 40 hours for each patient
  Sampling rate – 256Hz
  23 EEG channels
  International 10-20 system of EEG electrode positions
[1] Goldberger AL, Amaral LAN, Glass L, Hausdorff JM, Ivanov PCh, Mark RG, Mietus JE, Moody GB, Peng C-K, Stanley HE. PhysioBank, PhysioToolkit, and PhysioNet: Components of a New Research Resource for Complex Physiologic Signals. Circulation 101(23):e215-e220 [Circulation Electronic Pages; http://circ.ahajournals.org/cgi/content/full/101/23/e215]; 2000 (June 13).

## Slide 4: Spectral Analysis
Prior research indicates that spectral characteristics can be used to classify seizure events
The bands 0-16Hz and 16-25Hz are prominent
Preprocessing
  A low pass filter with a cut-off frequency of 25Hz and order of 50

## Slide 5: Spectral Analysis
Feature Extraction
  Spatial features – Manual selection (16 visually significant channels)
  Frequency features - Powers of 0-16Hz and 16-25Hz
  Temporal features – STFT with non-overlapping 4s window
Classifier
  SVM classifier with Radial Basis Function kernel
  Training Data
    65 seizure windows for cross validation
    22 seizure windows for testing
    41 seizure windows for testing
  1000 non seizure windows in both instances

## Slide 6: Spectral Analysis
Statistics of Patient 01
  65 seizure windows at 5 instances (11, 7, 11, 13, 23)
  20 hours of data were considered
Results – Cross Validation
  58 seizure windows out of 65 (accuracy ≈ 90%)
    First window or two of the seizure events were missed by the classifier
  8 false detections of onset (0.4h-1)
  Average latency – 5.4s
    Can be improved by a sliding overlapping window

## Slide 7: Spectral Analysis
Results – Training with 2 instances (22 seizure windows)
  37 seizure windows out of 65 (accuracy ≈ 58%)
    First window or two of the seizure events were missed by the classifier
    Regions within the seizure were missed by the classifier
  4 false detections of onset (0.2h-1)
  Average latency – 6.4s

## Slide 8: Spectral Analysis
Results – Training with 3 instances (41 seizure windows)
  50 seizure windows out of 65 (accuracy ≈ 77%)
    First window or two of the seizure events were missed by the classifier
    Regions within the seizure were missed by the classifier
  7 false detections of onset (0.35h-1)
  Average latency – 5.4s

## Slide 9: Wavelet Analysis
Discrete Wavelet Packet Transform – DWPT
  Improvement of DWT which represents more temporal and frequency information

## Slide 10: Wavelet Analysis
Pre-processing
  Low pass filter similar to spectral analysis
Feature extraction
  Wavelet packet decomposition
    5 levels
    Daubechies wavelet family – db4
  Obtain mean power of each packet (23 x 32 features)
  Temporal features – Non-overlapping window of 4s

## Slide 11: Wavelet Analysis
Dimensionality Reduction
  One-way ANOVA to obtain features with maximum significance (maximum p-value between seizure and non-seizure events)
  Dimensions reduced to 4
Classifier – Similar to spectral analysis

## Slide 12: Wavelet Analysis
Results – Cross Validation
  58 seizure windows out of 65 (accuracy ≈ 90%)
    First window or two of the seizure events were missed by the classifier – Similar to earlier instance
  7 false detections of onset (0.35h-1)
  Average latency – 2.4s
    Can be improved by a sliding overlapping window

## Slide 13: Wavelet Analysis
Results – Training with 2 instances (22 seizure windows)
  44 seizure windows out of 65 (accuracy ≈ 68%)
    First window or two of the seizure events were missed by the classifier – Similar to earlier instance
  2 false detections of onset (0.1h-1)
  Average latency – 5s

## Slide 14: Wavelet Analysis
Results – Training with 3 instances (41 seizure windows)
  56 seizure windows out of 65 (accuracy ≈ 86%)
    First window or two of the seizure events were missed by the classifier – Similar to earlier instance
  2 false detections of onset (0.1h-1)
  Average latency – 4s

## Slide 15: Discussion
Both approaches yield similar cross validation accuracies
DWPT based method yields high accuracy (90%) for less training data
High accuracy using very small number of features in DWPT
Low latency in DWPT method

## Slide 16: Improvements
Use other classifying methods
Further decrease features and maintain accuracy
Achieve even more accuracy
Introduce a correlation based feature extraction method
Test for variable window sizes and overlapping windows to reduce latency